## Slide 1: Uzbekistan’s electricity demand forecasting: an outlook until 2035 - Summary of results -
by Jente Mork, Dinara Saparova, Pavel Bilek
- Confidential draft as of 20.11.2024 -
UZBEKISTAN
N0 05 | NOV 2024

## Slide 2: Executive Summary
Rapid economic and population growth are driving changes in electricity use, also influenced by industrialization, transport electrification, and energy efficiency measures.
Furthermore, electricity consumption patterns are expected to shift due to factors such as increased industrialization, the electrification of transportation, and the implementation of energy efficiency measures.
Persistent supply shortages highlight the urgency of aligning capacity expansion with projected demand growth.
This study models electricity demand in Uzbekistan up to 2035, evaluating the potential impact of various economic and policy assumptions on the country’s electricity needs.
Electricity demand is expected to increase significantly in the coming years.
  Annual consumption forecasts range from 109 to 123 TWh in 2030 (+35-52%) and 131 to 151 TWh in 2035 (+62-87%).
  Peak demand is projected to reach 17.4 to 19.2 GW in 2030 (+41-56%) and 20.3 to 23 GW in 2035 (+64-86%)
External variables such as expectations on GDP growth, sectoral shifts, and tariff changes were found to significantly influence the projections.
To meet future electricity demand while supporting economic growth, this study identifies several direct and indirect implications for policy-making:
  Establish in-house forecasting capabilities, ensure robust capacity planning, maintain tariff reforms and leverage demand-side management tools.

## Slide 3: Structure
Introduction
Country context
Methodological approach
Data and model variants
Model results
Discussion of results
Implications for policy-making
Conclusion
Annex

## Slide 4: 1. Introduction
Rapid economic and population growth, alongside industrialization, transport electrification, and energy efficiency initiatives, are influencing future electricity consumption.
Accurate demand projections essential for appropriate capacity expansion planning.
This study models electricity demand in Uzbekistan up to 2035, evaluating the potential impact of various economic and policy assumptions on the country’s electricity needs.
Relevance of electricity demand forecasting
Policy planning
  Ensure adequate capacity expansion plans to align with projected demand growth.
  Incorporate policy measures to mitigate demand growth (e.g., energy efficiency measures).
Risk of underestimating demand
  Threatens energy security, potentially leading to blackouts and supply disruptions.
  Impacts daily life, industrial activity, and overall economic stability and growth.
Risk of overestimating demand
  Could result in inefficient allocation of resources and overinvestment in infrastructure.
  Emphasizes the need for strategic decision-making to ensure cost-efficient planning without excessive costs.
The study provides data-driven insights into Uzbekistan's electricity demand trends, enabling informed policy decisions.

## Slide 5: 2. Country context
Drivers of electricity demand
Rapid economic growth: Real GDP to reach UZS 1,055 trillion by 2030 (+45% from 2023)
Population expected to hit 43 million by 2030 (+22%), and urbanization on the rise
Industrialization and electrification trends expected to increase demand
Electricity sector challenges
Existing energy system already strained, with critical gaps in supply and challenges in regional transmission
Subsidised electricity tariffs limit incentives for energy savings and necessary investments in the energy system.
Implemented sector reforms
Tariff reform: higher tariffs and tiered system for households, promoting efficiency while protecting low-consumption users as a first step toward cost-reflective pricing.
Agency for Development and Regulation of the Energy Market to oversee sector liberalisation
Source: International Monetary Fund, World Economic Outlook, April 2024. United Nations, World Populations Prospects 2024. Note: GDP at constant 2020 UZS.
GDP in constant prices and population, 2000-2023
Annual electricity consumption, 2014-2023
Source: CDC Energiya.
Chart: UZS tn
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
GDP | 175290300000000 | 182652492000000 | 189958592000000 | 197936853000000 | 212584180000000 | 227465073000000 | 244524953000000 | 2.6775e+14 | 291852758000000 | 315492831000000 | 337873683000000 | 363299150000000 | 389102272000000 | 417493315000000 | 446191131000000 | 478400658000000 | 506780107000000 | 5.2905e+14 | 5.6016e+14 | 593667777000000 | 605514900000000 | 650343400000000 | 687240233000000 | 728398786000000
GDP growth (rhs) | 0.038 | 0.042 | 0.04 | 0.042 | 0.074 | 0.07 | 0.075 | 0.095 | 0.09 | 0.081 | 0.07094 | 0.07525 | 0.07102 | 0.07297 | 0.06874 | 0.07219 | 0.05932 | 0.04395 | 0.0588 | 0.05982 | 0.01996 | 0.07403 | 0.05673 | 0.05989
Chart: m
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Population | 24637755 | 24936354 | 25244211 | 25555748 | 25866770 | 26191930 | 26522019 | 26876068 | 27275948 | 27713601 | 28165056 | 28605957 | 29040434 | 29483372 | 29964758 | 30481229 | 31017464 | 31551672 | 32086683 | 32660298 | 33269104 | 33903640 | 34583751
Population growth (rhs) | 0.013305 | 0.01212 | 0.012346 | 0.012341 | 0.01217 | 0.012571 | 0.012603 | 0.013349 | 0.014879 | 0.016045 | 0.01629 | 0.015654 | 0.015188 | 0.015252 | 0.016327 | 0.017236 | 0.017592 | 0.017223 | 0.016957 | 0.017877 | 0.018641 | 0.019073 | 0.02006
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Electricity consumption | 54908140 | 56339107 | 57333996 | 60022400 | 62854796 | 65118348 | 69030000 | 74310000 | 77070000 | 80950000
Growth (rhs) | 0.026061 | 0.017659 | 0.04689 | 0.047189 | 0.036012 | 0.06007 | 0.076488 | 0.037142 | 0.050344

## Slide 6: 3. Methodological approach
Relevance of time frame
Short term: for dispatch planning (precise, detailed forecasts for hours/days)
Long-term: for generation adequacy and investment decisions over years
Forecasting method
Bottom-up: aggregates consumer data; high accuracy but data-intensive
Top-down: uses macro indicators (e.g., GDP, population); effective in data-scarce environments
Model chosen: Prophet
Open-source forecasting procedure
Captures long-term trends and multiple seasonal patterns (daily, weekly, yearly)
Integrates external variables (e.g., GDP) to improve prediction accuracy
Study provides long-term forecast on the national level, using the Prophet model and a top-down approach
Source: Own illustration.
Time frame
Short-term
Long-term
Forecasting method
Bottom-up
Top-down
Model selected: Prophet Advantages:
Handling of multiple seasonalities
Integration of external variables
User-friendly approach

## Slide 7: 4. Data and model variants
Forecast variable
Input: hourly national electricity demand from 2014 to 2023 (includes grid losses and own consumption by power plants)
Output: hourly demand (MW), capturing daily, weekly, and yearly demand patterns; total annual consumption (TWh), aggregated from hourly data
Model variants
Steady growth: GDP as a driver of demand
Sectoral expansion: Industrial, transport, and residential electricity demand included additionally as regressors
Tariff impact: Incorporates tariff elasticity for industry and residential consumption; includes adjustments made in 2023–2025, with real prices assumed stable 2026–2035
All: 2030-2035 consumption increased by 10%; assumption that supply expansion sufficient to meet previously unmet demand
Source: CDC Energiya.
Hourly electricity demand, 2014-2023
External variables included in each model variant
Sources: Own illustration.
Steady growth
GDP
Sectoral expansion
GDP
Sector-specific consumption
Tariff impact
GDP
Sector-specific consumption
Response of industry and households to higher prices
Model variant
External regressors
Chart: GW

## Slide 8: 5. Model results
Annual consumption (TWh)
Steady growth:
+45% 2023-2030, +69% by 2035
Reflects economic expansion with capacity improvements, moderate baseline growth
Sectoral expansion:
+52% 2023-2030, +87% by 2035
Higher demand due to industrialization and transport electrification, capturing sectoral dynamics
Tariff impact:
+35% 2023-2030, +62% by 2035
Demand moderation from expected price elasticity effects in response to recent and upcoming tariff adjustments
Peak demand (MW):
Parallel increase of +41-56% by 2030 and +64-86% by 2035
Results show influence of economic growth and sectoral shifts on electricity demand
Source: CDC Energiya (2014-2023 data); own calculations (projected data).
Annual electricity demand projection under the model variants
Sources: CDC Energiya (2023 data); own calculations (projected data).
 | Annual consumption (TWh) |  | 
2023 | 81.0 |  | 
 | Steady growth | Sectoral expansion | Tariff impact
2030 | 117.5 | 122.7 | 109.3
2035 | 137.2 | 151.5 | 130.9
 | Peak demand (GW) |  | 
2023 | 12.4 |  | 
 | Steady growth | Sectoral expansion | Tariff impact
2030 | 18.6 | 19.2 | 17.4
2035 | 21.2 | 23.0 | 20.3
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Actual | 54.9081 | 56.3391 | 57.334 | 60.0224 | 62.8548 | 65.1183 | 69.03 | 74.31 | 77.07 | 80.95
Steady growth | 80.9534 | 86.2032 | 91.0381 | 96.1584 | 101.3668 | 106.9726 | 112.0581 | 117.5266 | 121.4994 | 125.8289 | 129.3751 | 133.2759 | 137.1689
Sectoral expansion | 80.9534 | 86.268 | 91.4283 | 97.1273 | 103.0808 | 109.7686 | 116.4039 | 122.7064 | 128.6454 | 134.8873 | 140.2303 | 145.8831 | 151.4479
Tariff impact | 80.9534 | 81.7033 | 85.3172 | 89.62 | 94.1637 | 99.3997 | 104.6428 | 109.2983 | 113.9286 | 118.7634 | 122.7263 | 126.8917 | 130.9036
122.7117.5109.3
151.5137.2130.9
TWh
81.0

## Slide 9: 6. Discussion of results
Forecast comparison
2030 forecasts from "Steady growth" and "Sectoral expansion" align with external forecasts, both for annual convergence and peak demand.
Larger divergence by 2035 highlights different assumptions on development of electricity intensity.
Relevance for capacity planning
Ensure sufficient generation capacity to meet growing annual consumption.
Build system flexibility to handle peak load growth, especially as the share of renewables grows.
  Expand transmission, distribution and storage infrastructure to avoid supply bottlenecks (during demand surges)
Forecasts highlight the need to expand generation capacity and grid flexibility.
* China Electric Power Planning and Engineering Institute (EPPEI)
Sources: CDC Energiya (2023 data); Ministry of Energy, EPPEI* “Power System Planning Study in Uzbekistan, 2024” (external forecast range); own calculations (2030 and 2035 projections).
Forecast comparison for yearly consumption, 2030 and 2035
Sources: CDC Energiya (2023 data); EPPEI* “Power System Planning Study in Uzbekistan, 2024” (external forecast range); own calculations (2030 and 2035 projections).
Forecast comparison for peak load, 2030 and 2035
Chart: 
| 2023 | 2030 | 2035
Min | 118.2 | 150.8
External forecasts, range | 19.1 | 37.4
Steady growth | 80.95 | 117.5266 | 137.1689
Sectoral expansion | 122.7064 | 151.4479
Tariff impact | 109.2983 | 130.9036
TWh
Chart: 
| 2023 | 2030 | 2035
Min | 18.2 | 23.2
External forecasts, range | 2.9 | 5.75
Steady growth | 12.353 | 18.5475 | 21.1508
Sectoral expansion | 19.2195 | 23.0279
Tariff impact | 17.3958 | 20.2592
GW

## Slide 10: 7. Implications for policy-making
Build in-house forecasting capabilities
Establish a dedicated forecasting unit, e.g., within the Ministry of Energy, to improve energy planning and reduce reliance on external models.
Use local data on consumption, tariff elasticities and sectoral trends to refine demand projections.
Generation capacity planning
Ensure supply aligns with forecasted demand, accounting for technical uncertainties and potential capacity shortfalls. Include a 15-20% reserve margin due to the growing share of renewables.
Invest in transmission, distribution, and storage to manage renewable variability and peak loads.
Continue implementing cost-reflective tariffs
Implement cost-reflective tariffs to ensure efficient energy use and financial sustainability.
Strengthen regulatory oversight to ensure transparent pricing and investor protection.
Calibrate social support measures to protect low-income households while ensuring cost recovery.
Strengthen demand-side management (DSM)
Leverage digital tools like advanced metering infrastructure and real-time data analytics to enable more precise control over demand and allow implementation of time-of-use pricing.
Empower end-users with greater control over their electricity use, e.g., off-peak EV charging.
Provide grid operators with enhanced visibility into usage patterns, allowing for more efficient load balancing.

## Slide 11: 8. Conclusion
Uzbekistan's economy and population are growing rapidly, leading to a substantial increase in overall electricity consumption.
Furthermore, electricity consumption patterns are expected to shift due to factors such as increased industrialization, the electrification of transportation, and the implementation of energy efficiency measures.
Persistent supply shortages highlight the urgency of aligning capacity expansion with projected demand growth.
  While insufficient supply could stifle economic development, an overestimation could lead to excessive investment, potentially straining resources.
The study provides data-driven insights into Uzbekistan's electricity demand trends, enabling informed and sustainable policy decisions.
Electricity demand is expected to increase significantly in the coming years.
  Annual consumption forecasts range from 109 to 123 TWh in 2030 (+35-52%) and 131 to 151 TWh in 2035 (+62-87%).
  Peak demand is projected to reach 17.4 to 19.2 GW in 2030 (+41-56%) and 20.3 to 23 GW in 2035 (+64-86%)
External variables such as expectations on GDP growth, sectoral shifts, and tariff changes were found to significantly influence the projections.
The presented implications for policy-making aim to promote efficient, equitable access to electricity and strengthen Uzbekistan's energy security, while supporting economic growth.

## Slide 12: About the German Economic Team
Financed by the Federal Ministry for Economic Affairs and Climate Action, the German Economic Team (GET) advises the governments of Ukraine, Belarus*, Moldova, Kosovo, Armenia, Georgia and Uzbekistan on economic policy matters. Berlin Economics has been commissioned with the implementation of the consultancy. *Advisory activities in Belarus are currently suspended.
CONTACT Woldemar Walter, Project Manager Uzbekistan walter@berlin-economics.com German Economic Team c/o BE Berlin Economics GmbH Schillerstraße 59 | 10627 Berlin Tel: +49 30 / 20 61 34 64 0 info@german-economic-team.com www.german-economic-team.com Our publications are available under https://www.german-economic-team.com/en/uzbekistan/

## Slide 13: Annex
Hourly electricity consumption input data
January 25 to 27, 2022, are marked as outliers in the Prophet model: large-scale power outage that affected Uzbekistan, Kazakhstan, and Kyrgyzstan. In Uzbekistan, outage began around 11:00 a.m. According to the Ministry of Energy it took approx. 53 hours to fully restore electricity supply. Typical consumption patterns resumed on 28 Jan.
Prophet model specifications
The Prophet model was configured with daily, weekly, and yearly seasonalities, using Uzbekistan-specific holidays. To better capture recent trends, the number of changepoints was increased from 25 to 50, allowing the model to respond more effectively to shifts in electricity demand.
To evaluate forecast accuracy, we utilise the Mean Absolute Percentage Error (MAPE) metric (2014-2019 for training the model, 2020-2023 for testing). All variants achieve high accuracy with around 5.5% MAPE.
Prophet smooths irregular spikes, leading to narrower fluctuations in forecasts. To address potential underestimation of peak loads, we scale the 2023 hourly demand profile to match the projected 2030 annual demand, increasing peak load estimates by 11–16%. Therefore, peak loads are reported with a 16% increase.
Detailed assumptions of model variants
Increase forecasts after 2029 by 10%, as an estimated 10% of electricity demand goes unmet (Ministry of Energy).
Sectoral expansion:
Industrial electricity consumption: Future demand tied to industrial production (IP), with a coefficient based on 2010–2022 linear regression. IP growth (1.4x by 2026) follows Uzbek government targets (Development Strategy of Uzbekistan for 2022-2026), with post-2026 growth based on a five-year moving average.
Transport electricity consumption: Demand growth linked to population growth and increasing EV adoption, using coefficients from regressions based on 2000–2019 (population) and 2016–2019 (EV adoption). EV stock data and projections (2016-2029) are sourced from Statista; projections for 2030-2035 follow IEA global growth rates.
Residential electricity consumption: Demand modeled on population growth and GDP per capita, both with an elasticity of one. Population data from UN projections.

## Slide 14: Annex
Detailed assumptions of model variants (continued)
Tariff impact:
Electricity tariff reform 2023-2025
Industrial tariff
  Doubled from 450 to 900 UZS/kWh in 2023.
  Assumed to increase to 1000 UZS/kWh in 2025.
Household tariff
  295 UZS/kWh in 2023. Block tariff system for households introduced in 2024. Due to lack of detailed data, we assume 80% of households fall within Block I (450 UZS/kWh) and Block II (900 UZS/kWh), covering usage below 1,000 kWh/year. An average of Block I and II tariffs is used to approximate household costs under this structure (675 UZS/kWh).
  Block I and Block II assumed to increase to 600 and 1000 UZS/kWh in 2025 (average of 800 UZS/kWh).
After 2025: both nominal tariffs assumed to increase in line with inflation, keeping real tariffs stable.
Price elasticity assumptions
Elasticity values derived from established studies and reflect typical consumer behaviour in response to price changes in comparable markets.
Industrial demand: Price elasticity of -0.15 (10% tariff increase reduces demand by 1.5%).
Residential demand: Price elasticity of -0.1 (10% tariff increase reduces demand by 1%).